## Slide 1
Stages of clay

## Slide 2
Raw Clay/ Earthen Ware
-Clay that has not been processed (made into something)
-Can be premixed or found naturally

## Slide 3
Raw clay
Large water content
Very smooth and runny
Used to join two leather hard pieces of clay, attach handles and lids.
Can contain color and used as paint on plastic clay
-SLIP-

## Slide 4
Raw clay
Malleable (soft and easy to work with)
Most work, including construction and throwing, and slip decorating is done at this stage.
Plastic

## Slide 5
Clay is halfway dry.
Dry enough to handle and hold shape
Too dry to attach plastic clay to (different clay stages slapped together will cause cracking. slip may be used to attach two leather hard pieces together.
Good time to carve, apply fine decoration, smooth, and finish work
Leather Hard

## Slide 6
Clay is completely dry.
Most fragile stage. (handle with care)
No more work can be done.
Needs to be recycled or fired.
Clay ready to be fired is considered greenware
Bone Dry
Or
greenware

## Slide 7
Baking clay, usually in a kiln, which is like a big stove.
Temperature depends on the clay body.
What Does Firing Mean?

## Slide 8
Clay has been fired once (bisque firing)
Removes moisture, tightens body, and makes more sturdy
Clay is ready to be glazed or stained.
Bisque Ware

## Slide 9
Glaze Fired/Ceramic
Work has been Fired a second time in order to apply glaze or stain and/or to make ceramic non-porous.
Work may be done or re-fired with more glaze/stain

## Slide 10
Why do we wedge?
  Remove moisture
  Compact clay
  Even out clay (no hard or soft lumps)
  Remove air bubbles
Step One: Wedging
So Your Work Doesn’t
Go: BOOM!

## Slide 11
Images provided by Pinky’s Pottery.